## Slide 1: Working Group 7: Common test facilities
On behalf of USTC MPGD Group
6th DRD1 collaboration meeting, 09/10/2025
Test beam update and plans for
the μRGroove detector

## Slide 2: Micro-Resistive Groove detector
Completed the design, fabrication, and preliminary beam test of planar μRGrooves with dimensions of 10cm×10cm, 50cm×50cm, and 100cm×50cm.
Completed the design, fabrication, and beam test (including beam test in a magnetic field) of the cylindrical μRGroove prototype.
In November this year, detailed tests will be conducted on various planar μRGrooves, covering new structures and new setups.
Planar μRGroove
cylindrical μRGroove
Qixuan, 6th DRD1 Performance of c-uRGroove in magnetic field
Siqi, 5th DRD1 : Preliminary results of 50cmX50cm μRGroove
Siqi, Development of μRGroove detector

## Slide 3
Test1
Test3
Test2
Test4
The μRGroove detector for testing
4 mechanical frames, including 5 different μRGroove detectors：
Test1：100cm ×50cm μRGroove
Test2：50cm ×50cm μRGroove
Test3：10cm ×10cm μRGroove、10cm × 10cm small pitch μRGroove
Test4：10cm × 10cm 75μm-APICAL μRGroove

## Slide 4
Test1
Test content
Test2：50cm ×50cm μRGroove
Ar/CF4/CO2(45/40/15): CC&μTPC
Ar/iso-C4H10(90/10):
  High drift electric field (5kV/cm) for smaller Lorentz angle.
  Tilt at a small angle (5-6°) to simulate the Lorentz angle under 1Tesla, and verify the resolution of the CC or new algorithm
Test2
Test1：100cm ×50cm μRGroove
Ar/CF4/CO2(45/40/15):
  High-count-rate pion test
  μTPC test with tilt angle

## Slide 5
Test content
Test4：10cm ×10cm 75μm-APICAL μRGroove
Ar/CF4/CO2(45/40/15): CC&μTPC
Test3：10cm ×10cm μRGroove Tracker
Ar/CF4/CO2(45/40/15): CC&μTPC
Test3：10cm ×10cm small pitch μRGroove
Ar/CF4/CO2(45/40/15): CC&μTPC
Test3
Test4

## Slide 6: Summary
Thanks
Test different planar μRGrooves with different sizes and structures.
Two gases are required: Ar/CF₄/CO₂ (45/40/15) and Ar/iso-C₄H₁₀ (90/10). The latter is a flammable gas, and a matching iron box has been fabricated
Prioritize the testing of large-area detectors, especially under high-count-rate and high drift field.
For the μTPC, the test angles can be adjusted according to beam time, and it is sufficient to cover the range of 0-30°.