## Slide 1
Neutron Detectors
TPC readout with GridPix
Group 6
The Australian National University, Canberra, Australia
AstroCeNT, CAMK PAN, Warsaw, Poland
Laboratory of Instrumentation and Experimental Particle Physics, Coimbra, Portugal
University of Bonn, Germany
Victoria Bashu1, Diego Rodas2, Giorgio Canezin3, Maximilian Spors4
6th DRD1 Collaboration Meeting
October 10th, 2025
Notes: ‹#›

## Slide 2
Neutron Detectors
‹#›
  Outline
TPC and GridPix Basics
Experimental Setup
Results
Conclusions
Notes: ‹#›

## Slide 3
Neutron Detectors
‹#›
  TPC and GridPix Basics
Time Projection Chamber
  Components: A TPC consists of a large conversion and drift volume made of only gas, and a segmented readout plane;
  Working principle: Incoming particles passing or converting into charge particles ionize the molecules or atoms, the electrons drift to the readout plane;
  Key Features: Provides 3D tracking and particle identification by measuring the drift time and charge deposition (dE/dx).
Notes: ‹#›

## Slide 4
Neutron Detectors
‹#›
  TPC and GridPix Basics
GridPix
  Components: Combination of a highly pixelated readout ASIC and an integrated Micromegas Grid (InGrid);
  Working principle: Primary electron from the drift region enters a hole, gas amplification takes place and the complete avalanche is collected by a single pixel;
  Key Features: Provides excellent spatial and energy resolutions.
Source: DRD1 Lab book, DRD1 School 2025
Source: Jochen Kaminski
Notes: ‹#›

## Slide 5
Neutron Detectors
‹#›
  Experimental Setup
CLassroom Experiment On PArticle TRAcking (CLEOPATRA detector)
  The maximum drift length is 10 cm and the inner diameter of the drift volume is 8 cm,
  The anode side is equipped with 4 GridPix detectors, which are read out with the Scalable Readout System (SRS)
  Cosmic ray and radioactive source measurements
CLEOPATRA detector
Notes: ‹#›
Schematic and do transition

## Slide 6
Neutron Detectors
‹#›
  Experimental Setup
Cosmic ray measurements
  Scintillator surrounding the drift volume to trigger from the Cosmic rays
Setup with radioactive source
scintillator
Cosmic rays
Cosmic ray set up
Radioactive source
Scintillator for trigger
Notes: ‹#›
Schematic and do transition

## Slide 7
Neutron Detectors
‹#›
  Results
Drift velocity measurements with radioactive source Ar:CO2 82:18
Big thanks to Jochen Kaminski and Jan Glowcz
Notes: ‹#›

## Slide 8
Neutron Detectors
‹#›
  Results
Drift velocity from cosmic ray
Fit S-curve to find maximum drift time
Start fit at t> 8 µs to exclude distorted regions
  Reasons:
    Electron attachment (<1000 ppm Water present)
    Trigger inefficiencies for larger track
Notes: ‹#›

## Slide 9
Neutron Detectors
‹#›
  Results
Diffusion constants with cosmic ray dataset
Difference between drift time and time of arrival from the trigger
Pixel hit distance from the central cosmic ray track that is found by a track finding algorithm
Notes: ‹#›

## Slide 10
Neutron Detectors
‹#›
  Results
Diffusion constants
Charge distribution centered around 0
Orange points: spread of the gaussian of the corresponding slice (1D fit)
Readout pixel pitch 55 micron
Notes: ‹#›

## Slide 11
Neutron Detectors
‹#›
  Results
Energy resolution
Energy deposition has Landau distribution and not Polya as the amplification fluctuation is taken out by being able to count the primary ionised electrons from the track
Another way of viewing the spread of pixel hits from the central track
Closer to the track has most of the pixel hits
Pixel hits distances with respect to the central track
Notes: ‹#›

## Slide 12
Neutron Detectors
Thank you
‹#›
Big shout out to the organisers for this exciting and insightful experience
Notes: ‹#›