## Slide 1: Performance of C-μRGroove in magnetic field
Qixuan Huang
On behalf of USTC-MPGD Group
6rd DRD1-WG2, 7/10/2025

## Slide 2: Super Tau-Charm Facility
STCF is an e + e- collider operating at =2～7 GeV with a peak luminosity of cm-2s-1.
Collider Ring
1000m
Detector
Damping Ring
150 m
Track detection under extremely high luminosity requires the ITK performance includes:
  Ultra-Low Material Budget (<0.3%X0)
  Good Spatial resolution (<100μm)
  Handle high occupancy operated in μ-TPC mode
  ……
Possible Solutions：
3-layers Cylindrical MPGDs

## Slide 3: Cylindrical μRGroove
1st C- μRGroove prototype:
Size of active area: D=131.0mm, L=100.0mm;
Spatial resolution without magnetic field：
  <100μm for perpendicular tracks
  <120μm for Oblique incident tracks
Prototype
C-μRGroove
Next, Test detector performance in magnetic field

## Slide 4: Experiment setup
Goliath magnet at SPS-H4, B = 1T
Trackers: μRGroove, Ar/iC4H10(98/2), 3kV/cm drift field, Lorentz angle: ~6°
C-μRGroove: Ar/CF4/CO2(45/40/15), 0.5kV/cm drift field, Lorentz angle: ~22°
APV25 + SRS + mmDAQ
2025. 07

## Slide 5: Analysis Workflow of Raw Data
Beam Analysis Workflow
Waveform Process: extract charge and time with fit the leading edge
Clustering: group neighboring fired strips, allow one missing strip
Event Selection: allow only one hit per tracker, keep tracks with χ² < 10
DUT Matching: get hit point and find nearest cluster in the DUT
Reconstruct
~12 Adc
HitID for C-μRGroove
Track Slope

## Slide 6: Tracking System in magnetic field
μRGroove3
μRGroove2
μRGroove1
C-μRGroove
Align trackers by minimizing track residuals χ², mainly x/y translations and rotation around the z-axis.
Built track from μRGroove1 & 3, then compute residuals to μRGroove2 and estimate track error
Assume all trackers have the same spatial resolution ,
Estimate the track error(fitted from three trackers) via error propagation
C-μRGroove placed at the position with minimum
C-μRGroove position track error:
x: ~100 μm, y: ~66 μm

## Slide 7: Spatial resolution @B = 0T
Mid pos
Different hit positions lead to different incident angles through the cylindrical detector
Test the detector performance and determine the center position at B=0 T
Maybe wrinkle
charge centroid Residual RMS
Divide the cylindrical surface into regions along the arc per 2°
The center hard to determine accurately, but 2° error does not matter
1
2
region

## Slide 8: Charge-centroid @B = 1T
288
121
CC (Θ – Lorentz angle 0°) ≈ 70 μm correct for track error → consistent with B = 0 T.

## Slide 9: The micro-TPC mode
The time information of the hits can be used with the drift velocity to reconstruct
For large incident angles or with magnetic field, micro-TPC is stronger than the charge centroid
A new combination of CC and μTPC Method
Add the CC-reconstructed point as an extra point in the μ-TPC line fit
In the micro-coordinate, the extra point:
Provides more stable fits in low-statistics events while keeping μ-TPC advantages

## Slide 10: Time shift correction in magnetic field
Observed abnormal events, Indicates a timing shift affecting all points
Applying a global time offset to points during abnormal events
Origin residual distribution
corrected distribution
0 T
1 T

## Slide 11: Result in magnetic field
176
162
Micro-TPC
Combine of CC and Micro-TPC
At incident angle 0°: ~127 μm by μ-TPC (without track error)
New CC + μTPC combination improves resolution
Resolution degrades with increasing magnetic field

## Slide 12: Summary
Validation in Magnetic Field
Verified detector performance at B = 1 T
At normal incidence: <130 μm spatial resolution achieved
Proposed a new combination method, which further improves resolution